## Slide 1: DNS
Domain name service

## Slide 2: MEANING OF DNS
Developed in the 80’s by student at Berkeley University
BIOND (Berkeley Internet Name Domain is open source DNS Server that provides DNS service on Linux distributions
So, what is a DNS server? A DNS server is a service that helps to resolve a fully qualified domain name (FQDN) into an IP address and additionally, perform a reverse translation- translation of an IP address to a user-friendly domain name.
Why is name resolution important? Well, computers locate services on servers using IP addresses. However, IP addresses are not as user-friendly as domain names and it would be a big headache trying to remember each IP address that is associated with every domain name. A DNS server steps in and helps to resolve these domain names to computer IP addresses.

## Slide 3: PORT NUMBER
DNS USE PORT NO :- 53

## Slide 4: PURPOSE OF DNS
Names are easy to remember than numbers
The Domain Name System (DNS) is a method used to translate human readable domain names (or Fully Qualified Domain Names (FQDN)) to machine-readable IP addresses, to locate a computer in a network such as the Internet.

## Slide 5: FORWORD DNS
Resolving hostname to your IP address

## Slide 6: REVERSE DNS
Resolve IP address to Hostname

## Slide 7: Set Host Name
Set IP configuration
#nmcli connection add con-name india ifname enp0s3 type ethernet ipv4.add 192.168.1.2/24 gw4 192.1268.1.1 ipv4.dns 192.168.1.2 connection.autoconnect yes ipv4.method manual / nmtui
#hostname
#hostnamectl set-hostaname server1.example.com /nmtui

## Slide 8: Install Package
#yum install bind* -y {bind=Berkeley Internet Name Domain}

## Slide 9: Set Firewall
#firewall-cmd --permanent --add-service=dns
#firewall-cmd –reload
#firewall-cmd –list-all

## Slide 10: Edit Configuration Fille
#vim /etc/named.conf
option {
list-on port 53 { 127.0.0.1; server side ip add ; };
Allow-query { localhost; any; }
Zone “example.com “ IN {
Type master ;
file “for.example.com”;
allow-update { none; };
};
Zone “0.168.196.in –addr.arpa” IN {
type master;
file “rev.example.com”;
allow-update { none};
};

## Slide 11: CREAT FV &REV ZONE FILE
#cd /var/named
#cp -rvf named.localhost for.example.com
#cp -rvf forword.example.com rev.example.com

## Slide 12: Edit Forword Lookup Zone
#vim for.example.com
@ IN SOA server.example.com root .example.com (
as its
@ IN NS server.example.com
@ IN A SERVER IP
Un IN A DNS IP

## Slide 13: Edit reverse Lookup Zone
#vim rev.example.com
@ IN SOA server.example.com root.example.com (
as it is
3h )
@ IN NS server.example.com
@ IN A SERVER IP
UN IN A DNS IP
D.IP LAST IN PTR clint.example.com

## Slide 14: Change ownership
# chgrp root:named for.example.com
#chgrp root:named rev.example.com

## Slide 15: Check Configration
#named-checkconf -z /etc/named.conf

## Slide 16: Start and Enable service
#systemctl start named
#systemctl restart named
#systemctl enable named

## Slide 17: Verify
#ping host name
#ping ip
#ping google.com